## Slide 1
APPENDIX A1 — FULL ARCHITECTURE DIAGRAM
End-to-end data flow: device to EHR.
Edge / Incubator
FLIR Lepton 3.5
160×120 thermal sensor 9 Hz capture
P1–3
Coral Edge TPU
YOLOv8-Pose inference On-device processing
P1–3
Local Buffer
24h circular buffer SQLite + raw frames
P1–3
Transport
HL7v2 ORU
Observation Result Unsolicited message
P1
FHIR R4 REST
Observation resource HTTPS POST
P2–3
Capsule MDI
Medical Device Integration gateway
P1
Integration
Health Connect
Message broker Routing + transform
P1–3
IRIS for Health
FHIR repository Clinical data store
P2–3
Audit / Queue
Message persistence Compliance logging
P1–3
EHR / Clinical
Epic Flowsheet
CPTD as vital sign Zone temperatures
P1–3
BPA Alert
Best Practice Advisory Threshold-triggered
P2–3
SMART on FHIR
NeoTherm widget Trend + heatmap
P3

## Slide 2
APPENDIX A2 — HL7v2 MESSAGE FORMAT
ORU^R01 observation message for CPTD transmission.
MSH|^~\&|NEOTHERM|NICU_BED_3|
HEALTHCONNECT|NORTHWELL|
20260815143022||ORU^R01|
MSG00001|P|2.5.1
PID|1||MRN12345^^^MRN||
GARCIA^ELENA||20260101|F
OBR|1||ORD001|CPTD^Core-Periph
Temp Diff^NEOTHERM
OBX|1|NM|CPTD^Core-Peripheral
Temperature Difference^NEOTHERM
||2.7|degC|0.0-2.0|H|||F
OBX|2|NM|TCORE^Core Temp
^NEOTHERM||36.8|degC||||F
OBX|3|NM|TPERIPH^Peripheral
Temp^NEOTHERM||34.1|degC||||F
Transport
TCP/IP via Capsule MDI
Routing
Health Connect message broker
Frequency
Every 60 seconds (configurable)

## Slide 3
APPENDIX A3 — FHIR R4 OBSERVATION
Observation resource for CPTD.
{
"resourceType": "Observation",
"id": "cptd-20260815-143022",
"status": "final",
"category": [{"coding": [{"system":
"http://terminology.hl7.org/
CodeSystem/observation-category",
"code": "vital-signs"}]}],
"code": {"coding": [{"system":
"http://neotherm.io/fhir/codes",
"code": "cptd",
"display": "Core-Peripheral
Temperature Difference"}]},
"subject": {"reference":
"Patient/garcia-elena"},
"effectiveDateTime":
"2026-08-15T14:30:22Z",
"valueQuantity": {
"value": 2.7,
"unit": "degC",
"system": "http://unitsofmeasure
.org", "code": "Cel"},
"interpretation": [{"coding":
[{"code": "H",
"display": "High"}]}]
}

## Slide 4
APPENDIX A4 — REGULATORY DECISION TABLE
FDA classification analysis for each phase.
Question | Answer | Source
Is NeoTherm a medical device? | Phase 1: No (display only) Phase 2-3: Yes | 21 CFR 820
Does Phase 1 make a diagnosis? | No. Displays temperatures only. | FDA CDS Guidance 2022
Is CPTD a new biomarker? | No. Validated in literature since 1991. | Leante-Castellanos 2015
Does Phase 2 qualify for CDS exclusion? | Yes, if transparent + clinician review. | 21st Century Cures §3060
What class is Phase 3? | Class II (510(k) or De Novo) | FDA Product Code QMT
Is there a predicate device? | InSightIQ (DEN200063) — De Novo | FDA De Novo Database
Is the camera FDA-cleared? | FLIR Lepton is non-medical; system-level clearance needed. | FDA 510(k) Database
What about off-label thermal use? | 78% of NICU devices used off-label (AAP 2015). | AAP Technical Report
Who is the regulatory contact? | Taylir Speer — regulatory strategy lead. | Internal

## Slide 5
APPENDIX A5 — CLINICAL EVIDENCE
Published evidence supporting CPTD as a sepsis biomarker.
Claim | Evidence | Source
CPTD predicts sepsis 5h early | Core-peripheral temp gradient widened 5.2h before clinical diagnosis. | Leante-Castellanos 2015
83% sensitivity for LOS | CPTD >2°C had 83% sensitivity, 75% specificity for late-onset sepsis. | Leante-Castellanos 2015
Infrared matches contact probes | Non-contact IR agreed within 0.2°C of skin contact sensors. | Knobel-Dail 2017
CPTD correlates with NEC | Peripheral cooling preceded NEC diagnosis by 6–12 hours. | Ussat 2018
Works across all skin tones | Thermal IR emissivity 0.97–0.98 regardless of melanin content. | FLIR Technical Note 2020
Continuous > intermittent | Continuous monitoring detected 3x more hypothermic episodes. | Knobel-Dail 2017
Cost of missed sepsis | Each sepsis episode adds $170,000 in NICU costs. | Swanson 2018; Rolnitsky 2023
CPTD validated in premature + term | Studies include 24–40 weeks GA across multiple centers. | Multiple (see references)

## Slide 6
APPENDIX A6 — CONTRACT STACK
Nine agreements required before pilot deployment.
BAA
Business Associate Agreement
HIPAA-required for any PHI access
IRB Protocol
Institutional Review Board Approval
Display-only study Exempt or Expedited
IT Security
Northwell InfoSec Review
Network scan, pentest Data flow diagram
MSA
Master Services Agreement
Commercial terms Liability, IP, term
DUA
Data Use Agreement
De-identified data for ML training
Clinical Eng.
Biomed Engineering Approval
Electrical safety IEC 60601 testing
E&O Insurance
Errors & Omissions Professional Liability
$2M per occurrence $5M aggregate
Cyber Insurance
Cybersecurity Liability Coverage
Required by Northwell IT policy
Product Liability
General Liability + Product Coverage
Non-diagnostic claim reduces exposure
Adjunctive Tool Classification: Phase 1 is display-only, reducing insurance and liability requirements significantly.

## Slide 7
APPENDIX A7 — NORTHWELL INFRASTRUCTURE
Existing systems at Cohen Children’s Medical Center.
System | Role | Source
InterSystems Health Connect | HL7v2 / FHIR message broker, routing engine, audit log. | Northwell IT (confirmed by Zanos team)
Capsule MDI (Qualcomm) | Medical device integration gateway for bedside monitors. | Northwell Biomed Engineering
Allscripts Sunrise (current) | Current EHR at Cohen Children’s. Transitions to Epic May 2026. | Northwell CIO Office
Epic Hyperdrive (incoming) | New EHR. Flowsheet, BPA, SMART on FHIR support. | Epic Wave 2 deployment plan
InterSystems IRIS for Health | FHIR R4 data repository. Powers analytics + SMART apps. | Northwell Health AI team
EHR Transition: Cohen Children’s moves from Allscripts Sunrise to Epic Hyperdrive on May 30, 2026. Health Connect abstracts this transition — NeoTherm deploys once and messages route to whichever EHR is active. This is a core InterSystems value proposition.

## Slide 8
APPENDIX A8 — HARDWARE COST BREAKDOWN
Bill of materials: prototype to scale.
Component | Prototype Cost | At Scale (1000+)
FLIR Lepton 3.5 (160×120) | $250 | $120
Coral Edge TPU (USB) | $60 | $35
Raspberry Pi CM4 (4GB) | $65 | $40
Custom PCB + enclosure | $200 | $45
Power supply + cabling | $30 | $15
Assembly + QC | $150 | $20
TOTAL | $755 | $275
Volume | Unit Cost | Margin
1 (prototype) | $755 | N/A
10 (pilot) | $500 | 78%
100 | $350 | 86%
1,000+ | $275 | 90%+
<$1K
prototype unit
$275
at 1,000+ scale
90%+
gross margin at scale

## Slide 9
APPENDIX A9 — LENGTH-OF-STAY COST SAVINGS
Conservative model: earlier detection reduces LOS and cost.
Source: Swanson et al. 2018
• Neonatal sepsis episodes cost avg $170,927 more than matched controls • Average additional LOS: 22.4 days • Based on 41,666 NICU admissions across 348 US hospitals
Source: Rolnitsky et al. 2023
• Earlier empiric antibiotics reduced sepsis mortality by 23% • Each hour of delay increased mortality odds by 4% • Earlier treatment correlated with 18-25% shorter sepsis LOS
# NeoTherm LOS Savings Model
sepsis_cost = $170,927
sepsis_los = 22.4 days
cost_per_day = $7,630
los_reduction = 20% (conservative)
days_saved = 4.48 days
savings_per_ep = $34,185
nicu_beds = 50
sepsis_rate = 25%
admissions/yr = 800
episodes/yr = 200
TOTAL SAVINGS = $6,837,000/yr
PER BED = $136,740/yr
20%
LOS reduction (conservative)
$6,591
saved per patient
$213M
US-wide annual savings potential